Pumpkin Cell OS
Computer in Minecraft
CIMC Arch (16-bit)
Software Developer's Manual
Version 1.0
Copyright (c) SyberMCd 2020-2021
Copyright (c) Adam2004yt 2021
Prototype built by:
Adam2004yt
PumpkinCell
SyberMCd
# I. DEFINITIONS
## Shortcuts
- Op - Opcode (Operation Code)
- Mm - Mnemonic (in assembly)
- Args - Arguments (in assembly)
- AddB - Additional Byte (used for storing operation argument)
- CimcC - Instruction representation in CimcC language
- ia - Instruction Address
## Definitions
- Instruction – a well-defined, atomic task done by processor in specified time, called cycle time.
- Register – a small, CPU-internal storage with specified size.
- Virtual memory – the way in which the instructions “sees” the memory address space. It’s mapped to physical memory.
# PHYSICAL ARCHITECTURE
## Instruction Loader
        ,-----,
    Ack --| |
    D0 --| |
    D1 --| |
    D2 --| |
    D3 --| |
    D4 --| | [TODO]
    D5 --| |
    D6 --| |
    D7 --| |
    Rq --| |
    RqOn --| |
        '-----'
# Process
## CPU Cycle
See Control-Unit.mod
# Interrupts
## Internal Interrupts
If an interrupt is called, the registers are placed
on stack in the following order:
PUSH16 ip
PUSH8 flags
[PUSH16 arg]
'arg' is a 16-bit value which gives additional
information about interrupt.
If IRET is called, these registers are popped from
the stack in the reverse order. The arg must be
popped manually by operating system.
[POP16 arg] // done by OS
POP8 flags
POP16 ip
Table 1: Interrupts
No	Id	Arg	Mm	Purpose
0	INT0	no	#IM	Invalid Math Operation
1	INT1	no	#II	Invalid Instruction
2	INT2	no	#UE	Unspecified error
3	INT3	yes	#PF	Page fault / arg - [OPE0000|9b fault page] / OP – (0-Read,1-Write,2-Execute,3-Reserved) / E - If physical page exists
4	INT4	no	#R3	Reserved
5	INT5	yes	#R4	Reserved (arg is ignored)
6	INT6	no	#U1	User Accesible #1
7	INT7	no	#U2	User Accesible #2
8	IRQ0	no	#IQ0	Device Interrupt #0
9	IRQ1	no	#IQ1	Device Interrupt #1
10	IRQ2	no	#IQ2	Device Interrupt #2
11	IRQ3	no	#IQ3	Device Interrupt #3
12	IRQ4	no	#IQ4	Device Interrupt #4
13	IRQ5	no	#IQ5	Device Interrupt #5
14	IRQ6	no	#IQ6	Device Interrupt #6
15	IRQ7	yes	#IQ7	Cascaded Interrupt (reserved)

The User Accessible Interrupts can be called using an INT instruction.

The Cascaded Interrupt is reserved for scalability.

See Control-Unit.mod for further information.
# Registers
## General-Purpose Registers
Table 2: General-purpose registers
Mm	Size	Notes	Layout
ax	16b	Accumulator	[[-ah-] [-al-]]
bx	16b	Base	[[-bh-] [-bl-]]
cx	16b	Counter	[[-ch-] [-cl-]]
dx	16b	Data	[[-dh-] [-dl-]]
sp	16b	Stack pointer
bp	16b	Base pointer

## Control Registers
Table 3: Control Registers
Mm	Size	Notes
ip	16b	Instruction Pointer
flags	16b	Flags (effectively 8bit)
ivt	16b	Interrupt Vector Table Pointer
c0	16b	Control Register 0 (Paging descriptor)

### Flags Register
uuuuuuuurrPNZOGI u-unused bytes, r-reserved (do not change!)
I(Interrupt) G(Greater) O(Overflow) Z(Zero) N(In Interrupt) P(Paging)
## Internal CU Registers
These registers are not accesible by user.
Mm	Size	Purpose
addb	2b	Additional Byte Needed: / 0 (00) Not Needed N / 1 (01) 1 Byte Needed 1 / 2 (10) 2 Bytes Needed 2 / 3 (11) Not Checked -

# Virtual Memory
## Paging
If PF is set, all instructions uses virtual adresses. They are mapped to physical memory using Memory Management Unit.
The memory is divided into 512-byte pages.
Max addressable memory: 65536 B (16-bit address) / 128 pages (7-bit page ID)
Implementation: 8192 B / 16 pages
The virtual address is divided into parts:
0 4 7 8 16
+---------------#---------------+
| Page ID | Page Offset |
+-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
| PTidx |Pidx | Page-rel addr |
+-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
    | | |
    | | '------- (R) Address relative to page
    | '------------------- (P) Page index in Page Table
    '-------------------------- (PT) Page Table index in Page Directory
Physical address is calculated using following formula:
Phys = ((Pdaddr[PT].addr)[P]).addr = ((Pdaddr + *(PDaddress * 512 + PToffset * 4)].addr)[PTaddr + PIdx]).addr
        0 4 7 8 16
        +-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
        | PTidx |Pidx | Page-rel addr | Virtual address
        +-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
        | | |
        idx idx |
        | | |
        ,-------+-+-----+------, |
PD address >| PD | Page Table | |
        '----+----+---+--+-----' |
        | | | |
        '--off->-' | |
        ,--<--' |
        0 | 7 8 | 16
        +-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
        | Page ID | Page-rel addr | Physical address
        +-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
In result, the entire virtual address space is divided into 16 equal parts (each described by one page table). These parts are further divided into 8 equal parts (pages), each described by page table descriptor. This makes implementation using only 2 page tables.
## Enabling Paging
Paging is enabled by calling PGE instruction. The format of argument:
0 2 3 5 8 9 16
+-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
|Cps|L|Res| PDsiz | PD address |
+-+-+-+-+-+-+-+-#-+-+-+-+-+-+-+-+
  | | | | |
  | | | | '-------- Page Directory physical page number, in pages.
  | | | '------------------- Page Directory entry count - max 16
  | | '------------------------- Reserved
  | '---------------------------- Whether the data should be loaded from RAM - slow,
  | but needed at the first time. 0 can be used to
  | switch PDs.
  '------------------------------- Cache Index
## Page Directory
Page Directory has a maximum of 16 entries describing virtual memory divided into a maximum of 16 equal parts. It must be page-aligned. The real number of entries can be specified in PGE instruction (using PDsiz). The maximum size of PD is 16B.
Page Table descriptor in Page Directory:
0 1 8
+-+-+-+-+-+-+-+-#
|M| PT offset |
+-+-+-+-+-+-+-+-#
 | '-------- Page Table address offset (relative to PD address), in 4B-blocks. If
 | 0, #PF is triggered on access.
 '---------------- Mapped flag (If not set, the space will be considered identity-
        mapped)
Calculating address of page table descriptor in page directory:
PTaddr = PD address * 512 + PT offset * 4
## Page Table
Page Table is pointed by Page Directory entry and has 8 entries. It must be placed in the same page as Page Directory. The resulting size of Page Table is 8B.
Page descriptor in Page Table:
0 1 8
+-+-+-+-+-+-+-+-#
|P|Page physical|
+-+-+-+-+-+-+-+-#
 | '-------- Page Table physical address, in pages.
 '---------------- Present (should NOT crash when accessed)
Calculating address of page descriptor in page table:
Paddr = PTaddr + PIdx
Calculating resulting physical address:
Phys = Page physical * 512
## Page Directory Caching
When an instruction writes to c0, the Page Directory is loaded from RAM to cache specified by Cache Index (PDCI). The cache stores max. 4 page directories with their corresponding page tables.
Page Directory Cache size: 4 PDs * 16 PT descr * 1B/descr = 4x16x1B = 64B (16B)
Page Table Cache size: 4 PDs * 16 PTs * 8 Page descr * 1B/descr = 4x16x8x1B = 256B (64B)
Total size: 320B
Cache can be switched using PGE instruction, if L = 0.
# Assembly
## Detailed Description
### OUT16 a, b → 16-bit Output to Port
CimcC: __builtin_out16(a, b); // a-port, b-value
Reserved Opcode Range: 32 insn
x = port number (16x)
Op Mm Args
0x OUT16 ax -> *x
Pseudocode:
trig void out16(src16& data_source, u4 port)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    iostate state = io.output_data16(port, data_source);
    if(state.error)
        control.raise(#UE);
}
### OUT8 a, b → 8-bit Output to Port
CimcC: __builtin_out8(a, b); // a-port, b-value
Reserved Opcode Range: /3 (32 insn)
x = port number (16x)
Op Mm Args AddB
1x OUT8 al -> *x N
Pseudocode:
trig void out8(src8& data_source, u4 port)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    iostate state = io.output_data8(port, data_source);
    if(state.error)
        control.raise(#UE);
}
### IN16 a, b → 16-bit Input from Port
CimcC: b = __builtin_in16(a)
Reserved Opcode Range: /4 (16 insn)
x = port number (16x)
Op Mm Args AddB
2x IN16 ax <- *x 2(b)
Pseudocode:
trig void in16(dst16& data_destination, u4 port)
{
    if(!data_destination.allow_write())
        control.raise(#UE);
    iostate state = io_controller.input_data16(port, data_destination);
    if(state.error)
        control.raise(#UE);
}
### MOV a, b → Move Value from 'a' to 'b'
CimcC: a = b;
Reserved Opcode Range: /4 (16 insn)
Op Mm Args AddB Notes
30 MOV ax <= bx N
31 MOV ax <= dx N
32 MOV bx <= ax N
33 MOV bx <= dx N
34 MOV cx <= ax N
35 MOV cx <= dx N
36 MOV dx <= ax N
37 MOV dx <= [bx] N Read RAM at bx
38 MOV dx <= mem 2(b) Read RAM
39 MOV mem <= dx 2(a) Write RAM
3A MOV [bx] <= dx N Write RAM at bx
3B MOV ax <= flags N
3C MOV ax <= val 2(a)
3D MOV bx <= val 2(a)
3E MOV cx <= val 2(a)
3F MOV dx <= val 2(a)
Pseudocode:
trig void mov(dst16 data_destination, src16 data_source)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    if(!data_destination.allow_write())
        control.raise(#UE);

    data_destination = data_source;
}
### J*c a → Jump Conditionally
CimcC: if(...) __builtin_set_eip(a);
Jumps to 'a' if specific flags are set. Clears these flags.
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB Notes Alias
40 JMP ia 2(a) Unconditional
41 JZ ia 2(a) If ZF is set JE
42 JG ia 2(a) If GF is set
43 JL ia 2(a) If OF is set
44 JNE ia 2(a) If ZF is not set
45 JGE ia 2(a) If ZF or GF is set
46 JLE ia 2(a) If ZF or OF is set
47 .. Reserved ..
Pseudocode:
trig void jmp(iaddr address)
{
    if(!address.allow_jump_to())
        control.raise(#UE);

    instruction.jump_to(address);
}

trig void jz(iaddr address)
{
    if(control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jg(iaddr address)
{
    if(control.flags.GF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jl(iaddr address)
{
    if(control.flags.OF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jne(iaddr address)
{
    if(!control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jge(iaddr address)
{
    if(control.flags.GF || control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jle(iaddr address)
{
    if(control.flags.OF || control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}
### CMP a, b → Compare Values 'a', 'b'
CimcC: a ?? b;
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB
48 CMP ax =? dx
49 CMP bx =? dx
4A CMP cx =? dx
4B .. Reserved ..
4C CMP ax =? val 2(b)
4D CMP bx =? val 2(b)
4E CMP cx =? val 2(b)
4F CMP dx =? val 2(b)
### PUSH a → Push 'a' to Stack
 CimcC __builtin_push(a)
Reserved Opcode Range: (5 insn)
Op Mm Args AddB Notes
50 PUSH ax
53 PUSH dx
52 PUSHA All registries (ax,bx,cx,dx,sp,flags)
53 PUSH8 val 1(a) 1 byte
54 PUSH16 val 2(a) 2 bytes
### POP a → Pop from Stack to 'a'
 CimcC __builtin_pop(&a)
Reserved Opcode Range: (3 insn)
Op Mm Args Notes
55 POP ax 2 bytes
56 POP al 1 bytes
57 POPA All registries (ax,bx,cx,dx,sp,flags)
### ADD a, b → Add from 'a' to 'b'
 CimcC a += b;
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB
58 ADD ax <+ val 2(b)
59 ADD ax <+ bx
5A ADD ax <+ dx
5B ADD cx <+ val 2(b)
5C ADD cx <+ bx
5D ADD cx <+ dx
5E ADD sp <+ val 2(b)
5F ADD bp <+ val 2(b)
### SUB a, b → Subtract from 'a' to 'b'
 CimcC a -= b;
Reserved Opcode Range: /6 (4 insn)
Op Mm Args AddB
60 SUB ax <- val 2(b)
61 SUB ax <- bx
62 SUB ax <- dx
63 SUB cx <- val 2(b)
64 SUB cx <- bx
65 SUB cx <- dx
66 SUB sp <- val 2(b)
67 SUB bp <- val 2(b)
Sets:
 ZF if result == 0
 OF if result < 0 (result & 0x80 == 1)
 GF if result > 0
### MUL a, b → Multiply from 'a' to 'b'
 CimcC a *= b;
 Saves MSB -> DX, LSB -> AX
Reserved Opcode Range: /6 (4 insn)
Op Mm Args AddB
68 MUL ax <* val %> dx 2(b)
69 MUL ax <* bx %> dx
### DIV a, b → Divide from 'a' to 'b'
 CimcC a /= b;
 Saves modulus (a %= b) to DX
Using the opcode always triggers #IM if b == 0
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6A DIV ax </ val %> dx 2(b)
6B DIV ax </ bx %> dx
### AND a, b → Byte AND from 'a' to 'b'
 CimcC a &= b;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6C AND ax <& val 2(b)
6D AND ax <& bx
### OR a, b → Byte OR from 'a' to 'b'
 CimcC a |= b;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6E OR ax <| val 2(b)
6F OR ax <| bx
### NEG a → Byte/Logic Negate 'a'
 CimcC a = !a;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args Notes
70 NEG ax Byte Negate
71 NOT ax Logic Negate
### RET → Return from Procedure
 CimcC return; [__builtin_ip = *sp; __builtin_sp--;]
Reserved Opcode Range: /7 (2 insn)
Op Mm Notes
72 RET
73 IRET Return from Interrupt; clears IIF
### CALL a → Call Procedure
 CimcC (*a)(); [__builtin_ip = *sp; __builtin_jmp(a);]
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
74 CALL ia 2(a)
75 CALL ax N
### LIVT a → Load Interrupt Vector Table
 CimcC __builtin_livt(a);
Reserved Opcode Range: /8 (1 insn)
IVT structure:
0 4 8 16 8+16*size
+----+----+---------+---------+
|0000| Sz | Adresses x Size |

Op Mm Args AddB
76 LIVT ia 2(a)
### DBG → Debug Print
 CimcC __builtin_dbg();
Reserved Opcode Range: /8 (1 insn)
Note: If this instruction gets called in production
environment, it's considered an "Invalid Instruction".
The argument is used for debugging control unit and
is ignored.
Op Mm AddB
77 DBG 2(ignored)
### HLT a → Halt Processor
 CimcC __builtin_hlt();
Reserved Opcode Range: /8 (1 insn)
Op Mm
78 HLT
### EXT ... → Extended Operations
These opcodes are used to add new operations
in the future. They are reserved in current
version of spec. Using them triggers "Invalid
Instruction" trap.
Reserved Opcode Range: /7 (2 insn)
Op Mm
79 ...
### INT a → Raise Interrupt
 CimcC __builtin_int(a)
Reserved Opcode Range: /7 (2 insn)
Note: The user-callable interrupts are #U1 and #U2.
Op Mm Args
7A INT #U1
7B INT #U2
### NEG a → Byte/Logic Negate 'a'
 CimcC a = !a; a = -a
Reserved Opcode Range: /7 (2 insn)
Op Mm Args Notes
7C NEG ax Logic Negate
7D NOT ax Arithmetic Negate
### TRC a → Truncate a
 CimC a &= 0xFF
Reserved Opcode Range: /7 (2 insn)
Op Mm Args Notes
7E TRC ax Like mov al, ax
7F TRC dx Like mov dl, dx
### IN8 a, b → 8-bit Input from Port
 CimcC b = __builtin_in8(a)
Reserved Opcode Range: /4 (16 insn)
x = port number (16x)
Op Mm Args
8x IN8 al <- *x
### INC a → Increment a
 CimcC a++;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args
90 INC ax
### DEC a → Decrement a
 CimcC a--;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args
91 DEC ax
### XOR a, b → Exclusive OR from 'a' to 'b'
 CimcC a ^= b;
Reserved Opcode Range: /6 (4 insn) + /7 (2 insn)
Op Mm Args AddB Notes
92 XOR ax <^ val 2(b)
93 XOR ax <^ bx N
94 XOR ax <^ ax N Clear ax
95 XOR bx <^ bx N Clear bx
96 XOR cx <^ cx N Clear cx
97 XOR dx <^ dx N Clear dx
### AND a, b → Byte AND of Flags with 'b'
 CimcC __builtin_flags &= b;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args AddB
98 AND flags <& val 2(b)
### OR a, b → Byte OR of Flags with 'b'
 CimcC __builtin_flags |= b;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args AddB
99 OR flags <| val 2(b)
### PGE a → Enable Paging
 CimcC __builtin_paging_enable(a)
Reserved Opcode Range: /8 (1 insn)
Note: See Virtual Memory / Enabling Paging.
Op Mm Args
9A PGE ax
### MOV a, b → Move Value from 'a' to 'b'
 CimcC a = b;
Reserved Opcode Range: (5 insn)
Op Mm Args AddB
9B MOV ax <= [bp+x] 1(x)
9C MOV bx <= [bp+x] 1(x)
9D MOV cx <= [bp+x] 1(x)
9E MOV dx <= [bp+x] 1(x)
9F MOV bp <= sp
### XCHG a, b → Exchange Values
 CimcC __builtin_xchg(a, b);
Reserved Opcode Range: /4 (16 insn)
Op Mm Args AddB Notes
A0 XCHG ax <> ax N Debug
A1 XCHG ax <> bx N
A2 XCHG ax <> cx N
A3 XCHG ax <> dx N
A4 .. Reserved ..
A5 XCHG bx <> bx N Debug
A6 XCHG bx <> cx N
A7 XCHG bx <> dx N
A8 .. Reserved ..
A9 .. Reserved ..
AA XCHG cx <> cx N Debug
AB XCHG cx <> dx N
AC .. Reserved ..
AD .. Reserved ..
AE .. Reserved ..
AF XCHG dx <> dx N Debug
### Other Opcodes
Opcodes not listed here (B0-FF) are all reserved. If they are called, an Invalid Instruction trap is triggered.