PumpkinCell OS
Computer in Minecraft
CIMC 16-bit CPU Architecture (Cx16)
Software Developer's Manual
Version 1.0
Copyright (c) SyberMCd 2020-2021
Copyright (c) Adam2004yt 2021
Prototype built by:
Adam2004yt
PumpkinCell
SyberMCd
# Definitions
## Shortcuts
- Op - Opcode (Operation Code)
- Mm - Mnemonic (in assembly)
- Args - Arguments (in assembly)
- AddB - Additional Byte (used for storing operation argument)
- CimcC - Instruction representation in CimcC language
- ia – instruction address
## Definitions
- Instruction – a well-defined, atomic task done by processor in specified time, called cycle time.
- Register – a small, CPU-internal storage with specified size.
- Virtual memory – the way in which the instructions “sees” the memory address space. It’s mapped to physical memory.
# Physical Architecture
## Instruction Loader
        ,-----,
    Ack --| |
    D0 --| |
    D1 --| |
    D2 --| |
    D3 --| |
    D4 --| | [TODO]
    D5 --| |
    D6 --| |
    D7 --| |
    Rq --| |
    RqOn --| |
        '-----'
# Process
## CPU Cycle
See Control-Unit.mod
# Interrupts
## Internal Interrupts (Traps, Exceptions)
If an interrupt is called, the registers are placed on stack in the following order:
PUSH16 ip
PUSH16 flags
[PUSH16 arg]
'arg' is a 16-bit value which gives additional, interrupt-specific information about interrupt. If IRET is called, these registers are popped from the stack in the reverse order. The arg must be popped manually by operating system.
[POP16 arg] // done by OS
POP16 flags
POP16 ip
The User Accessible Interrupts can be called using an INT instruction.
The Cascaded Interrupt is reserved for scalability.
See Control-Unit.mod for further information.
## INT Argument
### Unspecified (fatal) error (#UE)
[0000CODE|RRRRRRRR]
CODE:
Code	Mnemonic	Meaning
0x0 (0000)	#RUE	Really unexpected error
0x1 (0001)	#IIR	Invalid IRET (interrupt underflow)
0x2 (0010)	#NMI	Non-Maskable Interrupt (Reserved)
0x3 (0011)		Reserved
0x4 (0100)		Reserved
0x5 (0101)		Reserved
0x6 (0110)		Reserved
0x7 (0111)		Reserved
0x8 (1000)		Reserved
0x9 (1001)		Reserved
0xA (1010)		Reserved
0xB (1011)		Reserved
0xC (1100)		Reserved
0xD (1101)		Reserved
0xE (1110)		Reserved
0xF (1111)		Reserved

R: Code-specific argument. If not required, it is 0.
### Page fault (#PF)
[XWE0000|9b faulting page]
- XW – (0 - Read, 1 - Write, 2 – Execute (Jump), 3 – Execute) → X – Execute, W – Write
- E – Whether physical page exists
### Reserved (#R4)
Argument is ignored and always set to 0.
### Cascaded Interrupt (#Q7)
Argument is ignored and always set to 0.
## Nesting Interrupt Handlers
Allowed order of nested interrupt handlers: No Interrupt → Interrupt Handler → Exception Handler
### Try To Raise (TTR) Interrupt Action
Interrupt source	EF	IIF	Is Raised	Result
Internal	0	0	YES	Jump to Exception Handler
Internal	0	1	YES	Jump to Exception Handler
Internal	1	0	NO	Double fault (crash)
Internal	1	1	NO	Double fault (crash)
External	0	0	YES	Jump to Interrupt Handler
External	0	1	NO	Ignore
External	1	0	NO	Ignore
External	1	1	NO	Ignore

### IRET Action
EF	IIF	Result
0	0	Raise #UE(#IIR) → Invalid IRET, Interrupt Underflow
0	1	IIF = 0; pop ISR data; jump to Interrupt Handler if raised → Normal IRET
1	0	EF = 0; pop ISR data; jump to Interrupt Handler if raised → Exception IRET
1	1	EF = 0; pop ISR data → Nested Exception IRET

## Interrupt Faults
When an exception occures when raising or returning from interrupt (especially if IVT is not set up or invalid, or IRET was called in invalid conditions), the following actions are taken:
### Interrupt Raise Fault Action
Interrupt source	EF	IIF	Result
Internal	0	0	Double fault (crash)
Internal	0	1	Double fault (crash)
External	0	0	Jump to Exception Handler → Fault on External Interrupt

### IRET Fault Action
EF	IIF	Result
0	0	Double fault (crash) → Interrupt Underflow
0	1	Raise relevant exception → Faulting Normal IRET
1	0	Double fault (crash) → Faulting Exception IRET
1	1	Double fault (crash) → Faulting Nested IRET

## Interrupt Vector Table
The IVT (Interrupt Vector Table) stores adresses of routines called when specific interrupt is raised.
The structure of IVT:
0 4 8 16 8+16*size
+----+----+---------+---------+
| Sz | Adresses x Size |
+----+----+-------------------+
Sz – The size of vector table, subtracted by 1. The value range is 0 – 255, which means that the IVT size range is 1 – 256.
Adresses – The interrupt entry adresses, ordered by INT number.
## Interrupt Reference
Table 1: Interrupts
No	Id	Arg	Mm	Purpose
0	INT0	no	#IM	Invalid Math Operation
1	INT1	no	#II	Invalid Instruction
2	INT2	yes	#UE	Unspecified (fatal) error
3	INT3	yes	#PF	Page fault
4	INT4	no	#R3	Reserved
5	INT5	yes	#R4	Reserved
6	INT6	no	#U1	User Accesible #1
7	INT7	no	#U2	User Accesible #2

All interrupt numbers greater than 7 are device interrupts. The PIC is automatically remapped to add 8 to its internal IRQ number, so that INT8 is equivalent to IRQ0, INT9 to IRQ1 etc.
In result, the CPU can handle up to 248 external interrupts.
# Registers
## General-Purpose Registers
Table 2: General-purpose registers
Mm	Size	Notes	Layout
ax	16b	Accumulator	[[-ah-] [-al-]]
bx	16b	Base	[[-bh-] [-bl-]]
cx	16b	Counter	[[-ch-] [-cl-]]
dx	16b	Data	[[-dh-] [-dl-]]
sp	16b	Stack pointer
bp	16b	Base pointer

## Control Registers
Table 3: Control Registers
Mm	Size	Notes
ip	16b	Instruction Pointer
flags	16b	Flags (effectively 8bit)
ivt	16b	Interrupt Vector Table Pointer

### Flags Register
uuuuuuuurEPNZOGI u-unused bytes, r-reserved (do not change!)
I(Interrupt) G(Greater) O(Overflow) Z(Zero) N(In Interrupt) P(Paging) E(In Exception Handler)
## Internal CU Registers
These registers are not accesible by user.
Mm	Size	Purpose
addb	2b	Additional Byte Needed: / 0 (00) Not Needed N / 1 (01) 1 Byte Needed 1 / 2 (10) 2 Bytes Needed 2 / 3 (11) Not Checked -

# Virtual Memory
## Paging
If PF is set, all instructions uses virtual adresses. They are mapped to physical memory using Memory Management Unit.
The whole physical and virtual memory is divided into 512-byte pages.
Max addressable memory: 65536 B (16-bit address) / 128 pages (7-bit page ID)
Implementation: 8192 B / 16 pages
The virtual address is divided into parts:

Physical address is calculated using following formula:
Phys = ((Pdaddr[PT].addr)[P]).addr = ((Pdaddr + *(PDaddress * 512 + PToffset * 4)].addr)[PTaddr + Pidx]).addr
Schematic:

In result, the entire virtual address space is divided into 16 equal parts (each described by one page table). These parts are further divided into 8 equal parts (pages), each described by page table descriptor. This makes implementation using only 2 page tables.
## Enabling / Configuring Paging
Paging is set up by calling PGE instruction. The format of argument:

## Page Directory
Page Directory has a maximum of 16 entries describing virtual memory divided into a maximum of 16 equal parts. It must be page-aligned. The real number of entries can be specified in PGE instruction (using PDsiz). The maximum size of PD is 16B.
Page Table descriptor in Page Directory:

Calculating address of page table descriptor in page directory:
PTaddr = PD address * 512 + PT offset * 4
## Page Table
Page Table is pointed by Page Directory entry and has 8 entries. It must be placed in the same page as Page Directory and be 4B-aligned. The resulting size of Page Table is 8B.
Page descriptor in Page Table:
0 1 8
+-+-+-+-+-+-+-+-#
|P|Page physical|
+-+-+-+-+-+-+-+-#
 | '-------- Page Table physical address, in pages.
 '---------------- Present (should NOT trigger #PF when accessed)
Calculating address of page descriptor in page table:
Paddr = PTaddr + PIdx
Calculating resulting physical address:
Phys = Page physical * 512
## Page Directory Caching
When a program calls PGE, the Page Directory is loaded from RAM to cache specified by Cache Index (PDCI). The cache stores max. 4 page directories with their corresponding page tables.
Page Directory Cache size: 4 PDs * 16 PT descr * 1B/descr = 4x16x1B = 64B (16B)
Page Table Cache size: 4 PDs * 16 PTs * 8 Page descr * 1B/descr = 4x16x8x1B = 256B (64B)
Total size: 320B
Cache can be switched using PGE instruction, if L = 0.
# CPU Identification
## CPUID Instruction
The CPUID instruction sets registries to CPU-specific information.
### AX Register
[NMMM AAAA:VVVV vvvv]
- ‘N’ – Has revision number in bx
- ‘M’ – Virtual Memory Capabilities
- ‘A’ – ALU Capabilities
- ‘V’ – Architecture major version (0x0 for cx8, 0x1 for cx16, 0x2 for cx32, 0x3 for cx64)
- ‘v’ – Architecture minor version (0x0 for cx16 Initial Release)
### Virtual Memory Capabilities
[RRRR]
‘R’ – Reserved
### ALU Capabilities
[1ISF]
- ‘1’ – Always set
- ‘I’ – 64-bit SIMD, see CPU/cx16-v2-SIMD.pdf
- ‘S’ – 32-bit SIMD, see CPU/cx16-v2-SIMD.pdf
- ‘F’ – Floating Point Coprocessor (FPC) implemented, see CPU/cx16-v2-FPC.pdf
# Assembly
## Detailed Description
### OUT16 a, b → 16-bit Output to Port
CimcC: __builtin_out16(a, b); // a-port, b-value
Reserved Opcode Range: 32 insn
x = port number (16x)
Op Mm Args
0x OUT16 ax -> *x
Pseudocode:
trig void out16(src16& data_source, u4 port)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    iostate state = io.output_data16(port, data_source);
    if(state.error)
        control.raise(#UE);
}
### OUT8 a, b → 8-bit Output to Port
CimC: __builtin_out8(a, b); // a-port, b-value
Reserved Opcode Range: /3 (32 insn)
x = port number (16x)
Op Mm Args AddB
1x OUT8 al -> *x N
Pseudocode:
trig void out8(src8& data_source, u4 port)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    iostate state = io.output_data8(port, data_source);
    if(state.error)
        control.raise(#UE);
}
### IN16 a, b → 16-bit Input from Port
CimcC: b = __builtin_in16(a)
Reserved Opcode Range: /4 (16 insn)
x = port number (16x)
Op Mm Args AddB
2x IN16 ax <- *x 2(b)
Pseudocode:
trig void in16(dst16& data_destination, u4 port)
{
    if(!data_destination.allow_write())
        control.raise(#UE);
    iostate state = io_controller.input_data16(port, data_destination);
    if(state.error)
        control.raise(#UE);
}
### IN8 a, b → 8-bit Input from Port
CimcC: b = __builtin_in8(a)
Reserved Opcode Range: /4 (16 insn)
x = port number (16x)
Op Mm Args
8x IN8 al <- *x
### MOV a, b → Move Value from 'a' to 'b'
CimcC: a = b;
Reserved Opcode Range: /4 (16 insn)
Op Mm Args AddB Notes
30 MOV ax <= bx none
31 MOV ax <= dx none
32 MOV bx <= ax none
33 MOV bx <= dx none
34 MOV cx <= ax none
35 MOV cx <= dx none
36 MOV dx <= ax none
37 MOV dx <= [bx] none Read RAM at bx
38 MOV dx <= [val] 2(b) Read RAM at mem
39 MOV [val] <= dx 2(a) Write RAM at mem
3A MOV [bx] <= dx none Write RAM at bx
3B MOV ax <= flags none
3C MOV ax <= val 2(a)
3D MOV bx <= val 2(a)
3E MOV cx <= val 2(a)
3F MOV dx <= val 2(a)
9B MOV ax <= [bp+x] 1(x)
9C MOV bx <= [bp+x] 1(x)
9D MOV cx <= [bp+x] 1(x)
9E MOV dx <= [bp+x] 1(x)
9F MOV bp <= sp none
Pseudocode:
trig void mov(dst16 data_destination, src16 data_source)
{
    if(!data_source.allow_read())
        control.raise(#UE);
    if(!data_destination.allow_write())
        control.raise(#UE);

    data_destination = data_source;
}
### J*c a → Jump Conditionally
CimcC: if(...) __builtin_set_eip(a);
Jumps to 'a' if specific flags are set. Clears these flags.
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB Notes Alias
40 JMP ia 2(a) Unconditional
41 JZ ia 2(a) If ZF is set JE
42 JG ia 2(a) If GF is set
43 JL ia 2(a) If OF is set
44 JNE ia 2(a) If ZF is not set
45 JGE ia 2(a) If ZF or GF is set
46 JLE ia 2(a) If ZF or OF is set
47 JMP ax none
Pseudocode:
trig void jmp(iaddr address)
{
    if(!address.allow_jump_to())
        control.raise(#UE);

    instruction.jump_to(address);
}

trig void jz(iaddr address)
{
    if(control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jg(iaddr address)
{
    if(control.flags.GF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jl(iaddr address)
{
    if(control.flags.OF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jne(iaddr address)
{
    if(!control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jge(iaddr address)
{
    if(control.flags.GF || control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}

trig void jle(iaddr address)
{
    if(control.flags.OF || control.flags.ZF)
        jmp(address);
    control.flags.clear_arith();
}
### CMP a, b → Compare Values 'a', 'b'
CimcC: a ?? b;
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB
48 CMP ax =? dx
49 CMP bx =? dx
4A CMP cx =? dx
4B .. Reserved ..
4C CMP ax =? val 2(b)
4D CMP bx =? val 2(b)
4E CMP cx =? val 2(b)
4F CMP dx =? val 2(b)
### PUSH a → Push 'a' to Stack
CimcC: __builtin_push(a)
Reserved Opcode Range: (5 insn)
Op Mm Args AddB Notes
50 PUSH ax
53 PUSH dx
52 PUSHA All registries (ax,bx,cx,dx,sp,flags)
53 PUSH8 val 1(a) 1 byte
54 PUSH16 val 2(a) 2 bytes
?? PUSH8 [bp+a] 1(a)
?? PUSH16 [bp+a] 1(a)
### POP a → Pop from Stack to 'a'
CimcC: __builtin_pop(&a)
Reserved Opcode Range: (3 insn)
Op Mm Args Notes
55 POP16 ax 2 bytes
56 POP8 al 1 bytes
57 POPA All registries (ax,bx,cx,dx,sp,flags)
### ADD a, b → Add from 'a' to 'b'
CimcC: a += b;
Reserved Opcode Range: /5 (8 insn)
Op Mm Args AddB
58 ADD ax <+ val 2(b)
59 ADD ax <+ bx
5A ADD ax <+ dx
5B ADD cx <+ val 2(b)
5C ADD cx <+ bx
5D ADD cx <+ dx
5E ADD sp <+ val 2(b)
5F ADD bp <+ val 2(b)
### SUB a, b → Subtract from 'a' to 'b'
CimcC: a -= b;
Reserved Opcode Range: /6 (4 insn)
Op Mm Args AddB Alias
60 SUB ax <- val 2(b)
61 SUB ax <- bx
62 SUB ax <- dx
63 SUB cx <- val 2(b)
64 SUB cx <- bx
65 SUB cx <- dx
66 SUB sp <- val 2(b)
67 SUB bp <- val 2(b) CPOP val
Sets:
 ZF if result == 0
 OF if result < 0 (result & 0x80 == 1)
 GF if result > 0
### MUL a, b → Multiply from 'a' to 'b'
CimcC: a *= b;
Saves MSB -> DX, LSB -> AX
Reserved Opcode Range: /6 (4 insn)
Op Mm Args AddB
68 MUL ax <* val %> dx 2(b)
69 MUL ax <* bx %> dx
### DIV a, b → Divide from 'a' to 'b'
CimcC: a /= b;
Saves modulus (a %= b) to DX
Using the opcode always triggers #IM if b == 0
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6A DIV ax </ val %> dx 2(b)
6B DIV ax </ bx %> dx
### AND a, b → Byte AND from 'a' to 'b'
CimcC: a &= b;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6C AND ax <& val 2(b)
6D AND ax <& bx
98 AND flags <& val 2(b)
### OR a, b → Byte OR from 'a' to 'b'
CimcC: a |= b;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
6E OR ax <| val 2(b)
6F OR ax <| bx
99 OR flags <| val 2(b)
### NEG a → Byte/Logic Negate 'a'
CimcC: a = !a;
Reserved Opcode Range: /7 (2 insn)
Op Mm Args Notes
70 NEG ax Byte Negate
71 NOT ax Logic Negate
### RET → Return from Procedure
CimcC: return; [__builtin_ip = *sp; __builtin_sp--;]
Reserved Opcode Range: /7 (2 insn)
Op Mm Notes
72 RET
73 IRET Return from Interrupt; clears: EF if it is set, IIF otherwise.
### CALL a → Call Procedure
CimcC: (*a)(); [__builtin_ip = *sp; __builtin_jmp(a);]
Reserved Opcode Range: /7 (2 insn)
Op Mm Args AddB
74 CALL ia 2(a)
### CALLA → Call Procedure and Setup Stack Frame
CimcC: __builtin_calla(ia); [push(bp); __builtin_call(ia); pop(bp)]
Reserved Opcode Range: /8 (1 insn)
Op Mm AddB
77 CALLA ia 2(ia)
.. CALLA ax none
### LIVT a → Load Interrupt Vector Table
CimcC: __builtin_livt(a);
Reserved Opcode Range: /8 (1 insn)
Opcodes:
Op Mm Args AddB
76 LIVT ia 2(a)
### HLT a → Halt Processor
CimcC: __builtin_hlt();
Reserved Opcode Range: /8 (1 insn)
Op Mm
78 HLT
### EXT ... → Extended Operations
These opcodes are used to add new operations in the future. They are reserved in current version of spec. Using them triggers "Invalid Instruction" trap.
Reserved Opcode Range: /7 (2 insn)
Op Mm
79 ...
### INT a → Raise Interrupt
CimcC: __builtin_int(a)
Reserved Opcode Range: /7 (2 insn)
Note: The user-callable interrupts are #U1 and #U2.
Op Mm Args
7A INT #U1
7B INT #U2
### INC a → Increment a
CimcC: a++;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args
90 INC cx
### DEC a → Decrement a
CimcC: a--;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args
91 DEC cx
### SHL a, b → Shift Left a by b
CimcC: a <<= b;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args AddB
90 SHL ax << val 1(b)
### SHR a, b → Shift Right a by b
CimcC: a >>= b;
Reserved Opcode Range: /8 (1 insn)
Op Mm Args AddB
91 SHR ax >> val 1(b)
### XOR a, b → Exclusive OR from 'a' to 'b'
CimcC: a ^= b;
Reserved Opcode Range: /6 (4 insn) + /7 (2 insn)
Op Mm Args AddB Notes
92 XOR ax <^ val 2(b)
93 XOR ax <^ bx N
94 XOR ax <^ ax N Clear ax
95 XOR bx <^ bx N Clear bx
96 XOR cx <^ cx N Clear cx
97 XOR dx <^ dx N Clear dx
### PGE a → Enable Paging
CimcC: __builtin_paging_enable(a)
Reserved Opcode Range: /8 (1 insn)
Note: See Virtual Memory / Enabling Paging.
Op Mm Args
9A PGE ax
### XCHG a, b → Exchange Values
CimcC: __builtin_xchg(a, b);
Reserved Opcode Range: /4 (16 insn)
Op Mm Args AddB Notes
A0 XCHG ax <> ax N Debug
A1 XCHG ax <> bx N
A2 XCHG ax <> cx N
A3 XCHG ax <> dx N
A4 .. Reserved ..
A5 XCHG bx <> bx N Debug
A6 XCHG bx <> cx N
A7 XCHG bx <> dx N
A8 .. Reserved ..
A9 .. Reserved ..
AA XCHG cx <> cx N Debug
AB XCHG cx <> dx N
AC .. Reserved ..
AD .. Reserved ..
AE .. Reserved ..
AF XCHG dx <> dx N Debug
### CPUID → Processor Identification
CimcC: __builtin_cpuid()
Reserved Opcode Range: /8 (1 insn)
Saves the CPU Identification (CPUID) data to registers.
Note: See CPU Identification.
Op Mm
?? CPUID
### Other Opcodes
Opcodes not listed here are all reserved. If they are called, an Invalid Instruction trap is triggered.